Stack smash gcc
Mordechi goodstein

---
Segment layout

---
Stack layout

---
Buf in stack

---
canarys

---
gcc diff

---
gcc stack-protector
-fstack-protector
        Emit extra code to check for buffer overflows, such as stack smashing attacks. This is done by
        adding a guard variable to functions with vulnerable objects. This includes functions that call
        "alloca", and functions with buffers larger than 8 bytes. The guards are initialized when a
        function is entered and then checked when the function exits. If a guard check fails, an error
        message is printed and the program exits.
-fstack-protector-all
        Like -fstack-protector except that all functions are protected.
-fstack-protector-strong
        Like -fstack-protector but includes additional functions to be protected --- those that have local
        array definitions, or have references to local frame addresses.
        NOTE: In Ubuntu 14.10 and later versions, -fstack-protector-strong is enabled by default for C,
        C++, ObjC, ObjC++, if none of -fno-stack-protector, -nostdlib, nor -ffreestanding are found.

---
static void __attribute__ ((constructor))
__guard_setup (void)
{
  unsigned char *p;
  int fd;
  if (__stack_chk_guard != 0)
    return;
#if defined (_WIN32) && !defined (__CYGWIN__)
  HCRYPTPROV hprovider = 0;
  if (CryptAcquireContext(&hprovider, NULL, NULL, PROV_RSA_FULL,
        CRYPT_VERIFYCONTEXT | CRYPT_SILENT))
    {
      if (CryptGenRandom(hprovider, sizeof (__stack_chk_guard),
        (BYTE *)&__stack_chk_guard) && __stack_chk_guard != 0)
        {
        CryptReleaseContext(hprovider, 0);
        return;
        }
      CryptReleaseContext(hprovider, 0);
    }
#else
  fd = open ("/dev/urandom", O_RDONLY);
  if (fd != -1)
    {
      ssize_t size = read (fd, &__stack_chk_guard,
        sizeof (__stack_chk_guard));
      close (fd);
      if (size == sizeof(__stack_chk_guard) && __stack_chk_guard != 0)
        return;
    }
#endif
  /* If a random generator can't be used, the protector switches the guard
     to the "terminator canary". */
  p = (unsigned char *) &__stack_chk_guard;
  p[sizeof(__stack_chk_guard)-1] = 255;
  p[sizeof(__stack_chk_guard)-2] = '\n';
  p[0] = 0;
}
How canarys are init?

---
How programs get run I
- the only system call that invokes a new program is execve()
- main(int Argc ,char **Argv,char** envp)
- struct linux_binprm
- struct linux_binfmt
  - names
- binfmt_script.c
  - recursion
- binfmt_misc.c
  - /proc/sys/fs/binfmt_misc

---
How programs get run II - ELF binaries
- FORMAT
  - PT_LOAD
  - PT_INTERP
  - PT_GNU_STACK
- fs/binfmt_elf.c.
  - flush_old_exec()
  - setup_new_exec()
  - setup_arg_pages(bprm,randomize_stack top(STACK_TOP),executable_stack);

---
getauxval() and the auxiliary vector
- LD_SHOW_AUXV=1 sleep 1
- #include <sys/auxv.h>
  - unsigned long int getauxval(unsigned long int type);
- AT_PLATFORM
- AT_RANDOM <==
- AT_EXECFN
- AT_ENTRY ???

---
glibc

---
glibc
_dl_random : csu/dl-sysdef.c
_libc_start_main : csu/libc-start.c
     we need to setup errno. */
  __pthread_initialize_minimal ();
  /* Set up the stack checker's canary. */
  uintptr_t stack_chk_guard = _dl_setup_stack_chk_guard (_dl_random); //memcpy
# ifdef THREAD_SET_STACK_GUARD
  THREAD_SET_STACK_GUARD (stack_chk_guard);
# else
  __stack_chk_guard = stack_chk_guard;
# endif

---
KERNEL
- task_struct stack_canary gs:014
- New – do_fork → copy_process → dup_task → tsk->stack_canary = get_random_int();
- Load - Syscall , switch_to
- Syscall
  - asm
  - syscall_trace_enter
  - Asm
  - syscall_table